## Slide 1
Compiler Installation Guide
Design of Intelligent SoC Robot
(aka Embedded Systems Design and Implementation)
http://ssl.kaist.ac.kr/class/18fall/socrobotdesign
Hoi-Jun Yoo
KAIST

## Slide 2: Intelligent SoC Robot Algorithm

## Slide 3: Brain Board Block Diagram

## Slide 4: Brain Board (Main Board)
Bottom
Top

## Slide 5: Brain Board (Main Board)
Bottom
Top

## Slide 6: Brain Board (Main Board)
Connector Pin Information

## Slide 7: SoC Brain Board Development Environment
PC
SoC Brain Board
USB Mini B-type Cable, 2ea
DC 5V Power Adapter (2A)
NTSC output Camera (12V)
Hardware
OS: Windows7(Recommended), Windows 8
Cygwin (gcc operation environment)
AE32000C Compiler
USB Download Program, USB Drive
Hyper Terminal (Putty)
Software

## Slide 8: Install Cygwin
Unzip cygwin_source.zip file
Execute cygwin_source/setup.exe
Set Root Directory to C:\Cygwin
Install For : All Users
Default Text File Type: Unix / binary Check
Install Cygwin
Next
Next

## Slide 9: Install Cygwin
Select Package : All Install
Install Cygwin
Next
Next
OK

## Slide 10: Install Other SW
Download AMAZON2_robot_v1.13.4_package.tar.gz
Brain board SW
Install Putty https://www.chiark.greenend.org.uk/~sgtatham/putty/latest.html
Install Putty

## Slide 11: Compiler Installation
Copy AMAZON2_robot_v1.13.14_package.tar.gz
to C:\cygwin\home\<user ID>
Compiler Installation

## Slide 12: Linux Command
Command | Description
ls | List directory contents
cd | Change the current directory
cp | Copy files or directories
mv | Rename or move files or directories
mkdir | Make a new directory
cat | Display file’s contents to the standard output device
tar | Store and extract files from a tarfile (.tar) or tarball (.tar.gz or .tgz)
pwd | Print the current directory
chmod | Change a file’s permissions
clear | Clear a command line screen/window
date | Display the system time

## Slide 13: Compiler Installation
Execute Cygwin
Type below command
  $ tar xvzf AMAZON2_robot_v1.13.4_package.tar.gz
Compiler Installation

## Slide 14: Compiler Installation
Move to other folder
  $ ls
  $ cd AMAZON2_robot_v1.13.4
  $ ls
Compiler Installation

## Slide 15: Compiler Installation
Toolchain unzip
  $ cd toolchain
  $ cp ae32000-elf-uclibc-tools-AE32000C-v2.6.4.tar.gz /usr/local
  $ cd /usr/local
  $ tar xfz ae32000-elf-uclibc-tools-AE32000C-v2.6.4.tar.gz
Compiler Installation

## Slide 16: Compiler Installation
Make shell file
  $ vi .bash_profile
Add following PATH to vi editor and save
  PATH=“${PATH}:/usr/local/ae32000-elf-uclibc-tools/bin”
Compiler Installation

## Slide 17: Compiler Installation
Verify installation
  $ source .bash_profile
  $ ae32000-elf-uclibc-gcc -v
Compiler Installation

## Slide 18: Driver Installation
Shift + restart
Click trouble shoot
Click advanced Options
Restart
USB Driver Installation
Disable driver signature enforcement

## Slide 19: Driver Installation
Connect mini B USB cable to COM1, COM2 port
USB Driver Installation
Power switch
USB port

## Slide 20: Driver Installation
Device manager  Other device  right click CP2102 USB to UART Bridge Controller
Update driver  Browse my computer for driver software
SELECT AMAZON2_robot_v1.13.4/tools/usb_to_serial_driver
USB Driver Installation

## Slide 21: Driver Installation
Device manager  Other device  Right click unidentified device
Update driver  Browse my computer for driver software
Browse  select AMAZON2_robot_v1.13.4/tools/usb_driver
Install driver
USB Driver Installation
Other device
Unidentified device
Universal Serial Bus controller

## Slide 22: Driver Installation
Connection type : Serial
Serial line : COM xx (get the number from device manager)
Speed : 115200
open
Putty Configuration
COM12

## Slide 23: Driver Installation
Ae32000c login: root
Then you can communicate with board
# usb_download
Kernal Ramdisk Installation

## Slide 24: Driver Installation
Move to AMAZON2_robot_v1.13.4/tools folder
Execute download_usb_nand.bat
Execute download_usb_image.bat
Kernal Ramdisk Installation

## Slide 25: Application SW
Open cygwin
Type below command
  $ cd AMAZON2_robot_v1.13.4/user_app/graphic_test
  $ make clean (delete every files)
  $ make (compile and generate executable file)
Application SW Complilation

## Slide 26: Application SW
Open folder AMAZON2_robot_v1.13.4/user_app/
Copy graphic_test file to AMAZON2_robot_v1.13.4/tools/
Open putty
  ae32000c login: root
  # usb_download
Execute AMAZON2_robot_v1.13.4/tools/RemoteManCLI.exe
Type below command to download file PC
  RemoteMan<‘q’ to exit> > target usb
  RemoteMan<‘q’ to exit> > rfw /mnt/f0/graphic_test graphic_test
  RemoteMan<‘q’ to exit> > run 0
※ rfw /mnt/f0/<file_name> <file_name>
※ if RemoteManCLI.exe does not identify the board, unplug and plug the USB cable
Download File (PC  Board)

## Slide 27: Application SW
Open putty
  ae32000c login: root
  # cd /mnt/f0
  # chmod 777 graphic_test (change graphic_test file to executable)
  # ./graphic_test (execute graphic_test file)
Execute File

## Slide 28: Application SW
Open putty
  ae32000c login: root
  # usb_download
Execute AMAZON2_robot_v1.13.4/tools/RemoteManCLI.exe
Type below command to download file PC
  RemoteMan<‘q’ to exit> > target usb
  RemoteMan<‘q’ to exit> > rfr /mnt/f0/graphic_test graphic_test
  RemoteMan<‘q’ to exit> > run 0
※ rfr /mnt/f0/<file_name> <file_name>
※ if RemoteManCLI.exe does not identify the board, unplug and plug the USB cable
Upload File (Board  PC)

## Slide 29: Application SW
Autoplay : Execute designated program after booting automatically.
Open putty
  ae32000c login: root
  # cd /mnt/f0
  # vi user_init
  Write below text to automatically execute hello file
  # chmod 777 user_init
App SW Autoplay
#!/bin/sh
Cd /mnt/f0
./hello &

## Slide 30: Demo SW
Demo SW Execution
Type m to start mean filtering
Type d to turn off direct camera

## Slide 31: Demo SW
Demo SW Execution
Type i to start color inversion
Type m to start mean filtering

## Slide 32: Demo SW
Demo SW Execution
What is front buffer?
What is back buffer?

## Slide 33: Single Buffering vs Double Buffering
Single Buffering
buffer
CPU continuously draw frame to buffer
Monitor continuously display frame from buffer
Monitor may display uncompleted frame
 tearing
frame
frame

## Slide 34: Single Buffering vs Double Buffering
Double Buffering
CPU continuously draw frame to back buffer
Monitor continuously display frame from front buffer
Monitor always display completed frame
Back buffer stores latest frame
frame
frame
Front buffer
Back buffer

## Slide 35: Single Buffering vs Double Buffering
Double Buffering
To display the latest frame, monitor should load frame from other buffer
Role of front buffer and back buffer changes
This is called flipping
frame
frame
Back buffer
Front buffer

## Slide 36: Single Buffering vs Double Buffering
Double Buffering
frame
frame
Back buffer
Front buffer
Type 5 to load AMAZON2.bmp
Type 6 to draw AMAZON2.bmp to back buffer

## Slide 37: Single Buffering vs Double Buffering
Double Buffering
frame
frame
Front buffer
Back buffer
Type 0 to flip back buffer and front buffer

## Slide 38: Single Buffering vs Double Buffering
Double Buffering
frame
frame
Front buffer
Back buffer
Type 2 to draw red rectangular to back buffer

## Slide 39: Single Buffering vs Double Buffering
Double Buffering
frame
frame
Back buffer
Front buffer
Type 0 to flip back buffer and front buffer

## Slide 40: Single Buffering vs Double Buffering
Double Buffering
frame
Back buffer
Front buffer
Type 1 to clear back buffer
frame

## Slide 41: Single Buffering vs Double Buffering
Double Buffering
frame
frame
Front buffer
Back buffer
Type 0 to flip back buffer and front buffer

## Slide 42: Demo SW
Demo SW Execution